Unit 8: Work, Power, and Simple Machines

Content Outline: Machines, Mechanical Advantage, and Efficiency (8.2)

- Machine

- This is a device that makes work easier by changing one or more of these factors:

- The amount of force exerted.

- The distance over which the force is exerted.

- The direction in which you exert the force.

- Terms associated with machines:

1. Input force - the force you exert on the machine.  You turning a screwdriver.

2. Output force - the force the machine exerts on an object.  The screwdriver on the screw.

3. Input distance - the distance over which the input force is exerted.

4. Output distance - the distance over which the output force is exerted.

5. Input work (IW) = input force x the input distance

6. Output work (OW) = output force x the output distance.

- Mechanical advantage

- This term refers to the number of times a machine increases a force exerted on it.

- Mechanical advantage = output force/input force

- When a Machine:

- Increases force - when the output force is greater than input force, so the mechanical advantage is

greater than one.

Example: Using a can opener: output force is 30 N and input force is 10 N so…

Mechanical advantage =  30N/10N= 3N

- Increases distance - increasing distance means that output force is less than input force, so the mechanical advantage is less than one.

Example: Output force is 10N and input force is 20N so…

Mechanical advantage = 10N/20N = 0.5N

3. Changes direction - when changing directions the input force will be the same as the output force so

mechanical advantage is equal to one.

- Efficiency of machines

- Efficiency compares output work to input work.

- Some work is wasted overcoming friction.

- Lower friction means that output work is closer to input work.

- Efficiency is expressed as a percentage.  The closer the percentage is to 100% the more efficient the machine is.

- Efficiency = (output work/input work) x 100%

Example: You do 250000J of work to cut a lawn with a push lawn mower.  If the work done by the

mower is 200,000 J, what is the efficiency of the mower?

So we know:

Efficiency = (output work/input work) x 100%

= (200,000 J/250,000 J)100% = 80%

- Real machines do not have an efficiency greater than or equal to 100%, some work is always lost to friction.  Such as a motor engine getting hot.

- Remember heat energy has very little ability to perform work… staying warm is a by product of

you (or another organism) breaking down energy molecules (food).

- Ideal machine if it existed would have an efficiency of 100% - input force equals output force.