Unit 5: Gas Chemistry
Content Outline: Solving Gas Pressure Problems (5.5)

I. 	Solving Gas Problems Involving Manometers
 	
            A.   When solving gas pressure problems involving either type of manometer,

Step 1: Convert the difference in the liquid level of the mercury from milliliters to kilopascals by

multiplying the difference by using the conversion factor:

__1 kPa__
                                                      7.501 mm
            Step 2: A. If the problem involves using a closed-arm manometer, the answer is simply the

difference in the mercury level converted to kilopascals.   
 	             B. If the problem involves using an open-arm manometer,  then either add or subtract

the difference (in kPa) to the given atmospheric pressure in problem.  
                                1. To determine whether to add or subtract the converted difference in the mercury

level depends on which arm the mercury level is higher in an open-arm

manometer.
                                     a.   If the mercury is higher in the arm connected to the gas, then the pressure

of the gas must be less than that of the atmosphere. As a result, the

pressure of the mercury (the difference in the liquid level) must be

subtracted from the atmospheric pressure to get the gas pressure.
                                     b.   If the mercury is higher in the open, or atmospheric, arm, then the pressure

of the gas must be greater than that of the atmosphere. As a result the

pressure of the mercury must be added to the given atmospheric pressure.

Problem Solving Hint: The greater the height of the liquid in one arm of a 
                               manometer is a measure of the greater pressure of the gas in the opposite arm.

II.         An Example of a Gas Pressure Problem and Solution                         
            
            A.   Determining the Pressure of a Gas

A open-arm manometer is filled with mercury. The mercury level is 6 mm higher in the arm of the

tube connected to the gas. What is the total pressure, in kilopascals, of the gas in the container if

the atmospheric pressure is 101.3 kPa?  

                   Solving Process

Step 1:  Convert the 6 mm difference in height to kilopascals (kPa).

                                                   6 mm       |       1 kPa____ = 0.8 kPa
                                                                   |    7.501 mm

                   Because the mercury is higher in the arm connected to the gas, the pressure                     
                   exerted by the gas must be less than that of the atmosphere.

Step 2:  In this case, we subtract the pressure of the mercury from the atmospheric pressure to

get the gas pressure.
                                                    
                                                     101.3 kPa – 0.8 kPa = 100.5 kPa

The total pressure of the gas in the container is 100.5 kPa.